SECTION 07 72 00

ROOF MOUNTED ATTIC EXHAUST VENT

**This is a CSI Three-Part Specification using CSI MasterFormat 2004-2010 Section Numbers and Titles.  This specification must be edited to suit your particular project.  Also, for your guidance in editing this master guide specification we have put in **Notes** below.  You may then delete these notes once editing is completed. **

**This section is based on the Lomanco Incorporated line of roofing ventilation.   For more information on Lomanco Inc. products and availability, or for the name of your local Lomanco, Inc. representative, contact us at the following: Lomanco, Incorporated, 2101 West Main Street, P.O. Box 519, Jacksonville, Arkansas  72076, 1-800-643-5593 phone,                  
(501) 982-1258 fax; or visit our website at: www.lomanco.com.**

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and 
		Supplementary Conditions and Division 01 Specification Sections, apply to 
		this Section.

1.2	SUMMARY

A.	Section Includes:

**Note: Delete roof accessories not used in project.**

1.	Roof mounted attic exhaust vents.

2.	Accessories.

B.	Related Sections:

**Note: Coordinate sections listed below with actual project requirements. **

1.	Section 07 31 13 - Asphalt Shingles

2.	Section 07 41 00 - Standing Seam Metal Roofing

3.	Section 07 51 13 - Built-Up Asphalt Roofing

4.	Section 07 52 13 - Modified Bituminous Membrane Roofing

5.	Section 07 53 23 - EPDM Roofing

6.	Section 07 54 19 - PVC Roofing

7.	Section 07 54 23 - TPO Roofing

8.	Section 07 61 00 - Sheet Metal Roofing

9.	Section 07 60 00 - Sheet Metal Flashing and Trim

10.	Section 07 71 00 - Roof Specialties

11.	Section 07 90 00 - Joint Sealants

12.	Section 09 91 13 - Exterior Painting

13.	Section 09 91 23 - Interior Painting

1.3	REFERENCE STANDARDS

**Note: Delete unnecessary references not used in project.**

A.	American Society for Testing and Materials:

1.	ASTM B 209/B 209M - Specification for Aluminum and Aluminum-
			Alloy Sheet and Plate.

2.	ASTM B 221/B 221M - Specification for Aluminum and Aluminum-
			Alloy Extruded Bars, Rods, Wire, Profiles and Tubes.

1.4	PERFORMANCE REQUIREMENTS

A.	General Performance: Roof mounted attic exhaust vents shall withstand 
		exposure to weather and resist thermally induced movement without failure, 
		rattling, leaking, or fastener disengagement due to defective manufacture, 
		fabrication, installation, or other defects in construction.

1.5	QUALITY ASSURANCE

A.	Certifications:

1.	Passed Miami-Dade County test requirements for structural uplift 
			and wind driven rain infiltration.  Miami-Dade County Approved - 
			NOA No.: 11-0602.04 expires 08/16/2016.

2.	Texas Department of Insurance “Windstorm” Approved - Product 
			Evaluation Report No.: RV-11.

1.6	ACTION SUBMITTALS

A.	Product Data: For roof mounted attic exhaust vent indicated.

B.	Sample: For each exposed product and for each color and texture specified, 
		prepared on Samples of size to adequately show color.

1.7	INFORMATIONAL SUBMITTALS

A.	Coordination Drawings:  Roof plans, drawn to scale, and coordinating 
		penetrations and roof-mounted items.  Show the following:

1.	Size and location of roof mounted attic exhaust vent specified in this 
			Section.

2.	Method of attaching attic exhaust vent to roof or building structure.

3.	Other roof mounted items including mechanical and electrical 
			equipment, ductwork, piping, and conduit.

1.8	DELIVERY, STORAGE AND HANDLING

A.	Store materials in a dry, well-ventilated, weathertight place.

1.9	COORDINATION

**Note: Coordinate with your project roofing requirements. **

A.	Coordinate layout and installation of roof mounted attic exhaust vent with 
		roofing membrane and base flashing and interfacing and adjoining 
		construction to provide a leakproof, weathertight, secure, and noncorrosive 
		installation.

B.	Coordinate dimensions with rough-in information or Shop Drawings of 
		equipment to be supported.

1.10	WARRANTY

A.	Manufacturer’s standard one year warranty for materials and 
		workmanship.

PART 2 - PRODUCTS

2.1	MANUFACTURER

A.	Basis of Design: Lomanco, Incorporated, 2101 West Main Street, P.O.        
		Box 519, Jacksonville, Arkansas  72076, 1-800-643-5593 phone,                  
		(501) 982-1258 fax, www.lomanco.com is specified.

2.2	ROOF MOUNTED ATTIC EXHAUST VENT

A.	Model “750-S Roof Louver”.

B.	Description: Slant-back style, self-flashing, roof mounted attic exhaust vent. 			Provided with manufacturer’s standard bird-proof construction, louvered 			sides seamed at top and top riveted securely to base flashing; three louvered 			sides open upward to prevent shingle discoloration; weather-tight collar, 			seamed to base flashing; large nailing flange.

C.	Materials:

1.	Aluminum: Conform to ASTM B 209;

a.	Base: 0.025” aluminum coiled sheet.

b.	Sides: 0.025” aluminum coiled sheet.

c.	Top: 0.025” aluminum coiled sheet.

d.	Collar: 0.0175” aluminum coiled sheet.

D.	Dimensions:  Overall 16” x 20-5/16” x 5” with hole size of 8”.

E.	Net Free Area: 50 square inches per unit.  **Note: Packaged 6 to carton.**

F.	Screens:  Manufacturer's standard, 16x18 aluminum mesh.

2.3	FINISHES

A.	Comply with NAAMM's "Metal Finishes Manual for Architectural and 
		Metal Products" for recommendations for applying and designating finishes.

B.	Appearance of Finished Work:  Noticeable variations in same piece are not 
		acceptable.  Variations in appearance of adjoining components are 
		acceptable if they are within the range of approved Samples and are 
		assembled or installed to minimize contrast.

C.	Finish:  Manufacturer’s standard, factory applied, embossed, baked on 			“Valspar Super Flex” polyester paint with minimum 0.8 top coat and 
		minimum 0.3	wash coat.

1.	Colors Available: Brown, White, Black, Weathered Bronze, Forest 
			Green, and Milled Finished Aluminum.

PART 3 - EXECUTION

3.1	EXAMINATION

A.	Examine substrates, areas, and conditions, with Installer present, to verify 
		actual locations, dimensions, and other conditions affecting performance of 
		the Work.

B.	Verify that substrate is sound, dry, sloped for drainage, and 
		securely anchored.

C.	Verify dimensions of roof openings for roof mounted attic exhaust vents.

D.	Proceed with installation only after unsatisfactory conditions have been 
		corrected.

3.2	INSTALLATION

A.	General:  Install roof mounted attic exhaust vents according to 
		manufacturer's written instructions.

1.	Install level, plumb, true to line and elevation, and without warping, 
			jogs in alignment, excessive oil canning, buckling, or tool marks.

2.	Anchor securely in place so they are capable of resisting indicated 
			loads.

3.	Use fasteners, separators, sealants, and other miscellaneous items as 
			required to complete installation of roof mounted attic exhaust vents 
			and fit them to substrates.

4.	Install roof mounted attic exhaust vents to resist exposure to weather 
			without failing, rattling, leaking, or loosening of fasteners and seals.

B.	Metal Protection:  Protect metals against galvanic action by separating 
		dissimilar metals from contact with each other or with corrosive substrates 
		by painting contact surfaces with bituminous coating or by other permanent 
		separation as recommended by manufacturer.

1.	Coat concealed side of exhaust ventilator with bituminous coating 
			where in contact with wood, ferrous metal, or cementitious 
			construction.

2.	Underlayment:  Where installing exhaust ventilator directly on 
			cementitious or wood substrates, install a course of felt underlayment 
			and cover with a slip sheet, or install a course of polyethylene sheet.

3.	Bed flanges in thick coat of asphalt roofing cement where required by 
			manufacturer of exhaust ventilator for waterproof performance.

C.	Attic Exhaust Ventilator Installation:  Verify that roof mounted attic exhaust 
		ventilators operate properly and have unrestricted airflow.  Clean, lubricate, 
		and adjust operating mechanisms.

3.3	REPAIR AND CLEANING

**Note: Retain paragraph below for galvanized-steel surfaces. **

A.	Galvanized Surfaces:  Clean field welds, bolted connections, and abraded 
		areas and repair galvanizing according to ASTM A 780.

**Note: Retain paragraph below for primed surfaces. Coordinate section numbers with your project requirements**

B.	Touch up factory-primed surfaces with compatible primer ready for field 
		painting according to Section 09 91 13 - Exterior Painting and 
		Section 09 91 23 - Interior Painting.

C.	Clean exposed surfaces according to manufacturer's written instructions.

D.	Clean off excess sealants.

E.	Replace ventilators that have been damaged or that cannot be 
		successfully repaired by finish touchup or similar minor repair procedures.

END OF SECTION